Impulse Programming Design 2014

The “Time” in Impulse

Contributors:
Jerry Fan
(add yourself)

Note on versioning
Due to programming practices started in a previous robotics season, programs have a version number attached to them. The version corresponds to development of the program itself, therefore it is relevant to title design entries under version rather than date. Each version has different design intention.

# TimeV1
Code was created for simple control of robot using joystick, drawing from previous season's user control idea of requesting input and storage into variable, modification of variable, and output to motors. The robot was physically complete and ready for the first scrimmage at this point.
Output
Variable
Input
Modifications

Simple time based autonomous functions have been imported over from last season, and adapted for use by changing ports. Time based functions are used as no sensors have been attached onto the robot. Currently all autonomous does within a match was initialise the robot for user control.

Additional controls available are:
- Intake movement
- Lift movement
- Straight drive
- Turning drive
- Strafing drive

It was doubtful any other team will have a proper autonomous set up as they would have been concentrating on getting a robot up and running for the first scrimmage. Wiring on the robot should be optimal with a 50/50 split on each half of the cortex. It was found last season that the micro-controller had a current limit, and power needs to be as even as possible for best results in ports 1-5 and 6-10. This version of the program was used in the first scrimmage.

# TimeV2
TimeV2 was created with the idea of a fully working autonomous and additional user control features that would match last season's. Starting with the addition of sensors and a rework of the lift, the physical robot was much improved.
Available sensors:
- Potentiometer on left lift axle
- Potentiometer on right lift axle
- Shaft encoder on front left drive axle
- Shaft encoder on front right drive axle

With these, last year's code was fully imported into the current program. Pre second scrimmage changes in sensors include the upgrading of shaft encoders to integrated shaft encoders and the loss of one potentiometer on the lift due to hardware breakages. Another potentiometer was added as a manual switch to help the program determine which side the Skyrise claw was on, a new addition to the robot.
Additional sensors:
- Shaft encoder on back left drive motor
- Shaft encoder on back right drive motor
- Potentiometer attached to base as switch
## Autonomous function development
The drive autonomous